# Tadarida-L User Manual

## Software Installation

To install Tadarida-L under Windows (from XP to 8.1), you must download:
https://github.com/YvesBas/Tadarida-L/archive/master.zip
Note that Tadarida-L had not been ported to Linux.

Decompression and downloaded zip file contains two directories:
- Sources
- Install

Executing TadaridaL.exe from the install directory will start the software.

## Build

If you wish to read and modify TadaridaL sources, and then build it, use “sources” subdirectory of the install download (see above).
These sources have been built with Qt 5.5.
To run the build, you must copy all files from the install subdirectory (see above), of course except TadaridaL.exe.
.dll files from Qt libraries (such ase Qt5core.dll) are not necessary if the Qt bin directory is added to environment variable “PATH”.

## Software function
TadaridaL software runs on Windows (at least from Vista to Windows 8.1).
It runs on two different modes: simple (default) and extended.
To run the extended mode, you must edit the config.ini file within config subdirectory of the installed software, to “mode=1”.
This config.ini memorizes all the options precedently selected.
The parameter modifyFreq = 1 allows the user to choose between two frequency modes: high frequencies (8 to 250 kHz)and low frequencies (0.8 to 25 kHz).

### Treatment of sound files
This part is the only one accessible in simple mode and corresponds to the left half of the window in extended mode (see above).

### User settings

#### Time expansion
Two groups of radio button propose three processing mode:
- “x10” for 10-times expanded recordings, commonly used when recording ultrasounds and bats
- "x1" for direct/real-time recordings
- “Ignore” if one of the channel is to be ignored in the processing.
This choice is separated between left and right channel because some ultrasound detectors output gives a stereo “extended + direct” sound (e.g. Tranquility Transect© from Courtpan Design Ltd)

Note that TadaridaL does not process directly stereo recordings but only short (see below) and mono recordings. It has originally been designed to read splitted channel codes from Kaleidoscope© software (Wildlife Acoustics). For that reason, TadaridaL basically considers all .wav files to be from a left channel except if they contain the three characters chain “_1_” that identify the “right channel” in Kaleidoscope output.
« .wav files » must be short. Accepted limit depends on sound file characteristics (between 6.4 and 12.8 seconds in high frequency mode, and between 32 and 64 seconds in low frequency mode).
This limit is necessary for memory consumption and performances of Tadarida-D and Tadarida-C. We recommand treating sound files of no more than 5 seconds duration if a large number of species co-occur in time. The ability of Tadarida-C to correctly classify species indeed decreases with the number of species vocalizing within the file.

#### Frequency mode
This setting defines the frequency interval between which sound events will be detected
- High frequency: sound events whose peak frequency is comprised between 8 and 250 kHz (e.g. for bats and bush-crickets)
- Low frequency: sound events whose peak frequency is comprised between 0.8 and 25 kHz (concerns most animal vocalizations)
Note that minimum and maximum frequencies of detec ted sound events (DSEs) could exceed these range limits and that only the master point frequency (elements with maximum energy within the DSE) is used as a filter.
The two frequency modes imply different Fast Fourier Transformation settings to obtain an optimal trade-off between time and frequency resolutions.
High frequency: 0.2-0.4 ms and 0.6-1.2 kHz
Low frequency: 2-4 ms and 60-120 Hz

#### Parallelism
A scroll bar allows to define the number of threads to be run simultaneously, from 1 to 8 (default 4).
Note that a thread uses approximately 150 MB memory.

#### Advanced settings
This button appears only in extended mode and allows to modify some sensitive parameters of the detection process.
Note that default settings have been carefully optimized by authors and any modification of these makes the use of subsequent Tadarida-C very hazardous.
- Detection and stop threshold correspond to the hysteresis threshold used to detect and delimit sound events (see technical details below about shapesDetect method).
- p_nbo indicates the fraction of FFT window size between a window and the following one. This corresponds to overlap setting in FFT. For example, 4 (default) mean (1-1/4)= 75 % of overlap. Increasing this setting will increase time response, and decreasing it will diminish information collected on DSEs, especially the most frequency-modulated ones. The default value is considered as an optimal trade-off by the authors
- Treatment of silences indicates if the CorrectNoise should ignore silence period or not (see below CorrectNoise method for details)
- Percentage q5 determines the percentile value of amplitude, determining the floor of background noise on each frequency band. The default value (5 %) is a trade-off between false positive rate (increasing with lower values) and false negative rate on narrowband insects (increasing with higher values).
- Minimum pixel number q is a “watchdog” preventing background noise level to be calculated on a too small number of elements if the .wav file is very short. It gives the minimum number of elements (=pixels) to be used for calculated background noise floor, even if it is superior to the given percentile (see Percentage q5 above). For example, if a short .wav files is constituted by 100 FFT windows, the default values of these last two parameters (respectively 5% for the percentiles and 10 minimum number of pixels), the background noise floor will be calculated with the 10 lowest values instead of the 5 (=5%).
- Parameters version allows to go back to previous version of features list. 0 corresponds to 180 first features developed (=preliminary 2014 version), 1 corresponds to the 151 features selected for Vigie-Chiro users (i.e features used in Vigie-Chiro classifier, https://vigiechiro.herokuapp.com)
- Deactivate CorrectNoise allows to switch off the CorrectNoise method

da2 and jpg files
This check box, available only in the extended mode, allows to create supplementary output necessary for the labelling of reference sounds (see below)

Include subdirectories
This checkbox allows to run the detection process on several .wav files directories contained within the selected directory (see below)

#### Folder containing wav files
A « Browse » button allows to select the directory containing the .wav files to be processed.
Alternatively, the directory path can be copied and pasted within the text box.

#### Run / Cancel
The “Run” and “Cancel” buttons respectively allow to start and stop the process.

At the end of the process, an automatic message gives the number of treated and ignored files (and explaining the cause for the latters).
Detailed errors sources are stored in "error.log" file within the “txt” subdirectory
Other .log files are stored in this directory for maintenance purpose.
A version.ini is also stored within the treated .wav files directory. It ensures compatibility between the detection and the labelling processes.

### Main outputs

#### ".ta" files

In a « txt » subdirectory, a «.ta » file appears for each .wav file. In a simple tab separated text format, you will find all the features extracted from the DSEs (see appendix below). First line gives the column headers, and each following line the value of each features for each sound event detected (basically, one line per DSE).
First columns are:
Filename: name of .wav file simple tab separated text format
CallNum: sound event identifier (integer)
Version: detection process version (see below)
FileDur: .wav file duration
SampleRate: .wav file sample rate
Following columns give each features computed for each DSE (see appendix below)

#### “.da2” files

In a « dat » subdirectory, a «.da2 » file appears for each .wav file (if the “da2 and jpg” checkbox is checked, see above). It contains information about the delimitation in frequency and time of each DSE. This information is noticeably used each time the detection process is modified to match every previously DSEs to newly DSEs, and thus ensures compatibility of collected reference sound data with future versions.

#### ".jpg" files

In a « ima » subdirectory, a «.jpg » file appears for each .wav file (if the “da2 and jpg” checkbox is checked, see above). It contains an image of the spectrogram the .wav files to be used in the labelling interface. Note that elements contained within DSEs are displayed in a pink amplitude gradient whereas elements outside DSEs are displayed in a blue amplitude gradient.

## Labelling

The labelling interface is available only in the extended mode (right half window). It allows advanced users to constitute reference sound database (RSDB) and subsequently build their own classifier (see Tadarida-C manual).
 [copie d'écran de TadaridaL en mode étendu mettant en valeur la partie droite]

### Database folder
At the first execution of the extended mode, user will be asked to give a directory path where each reference .wav file will be stored with its associated files.
Reference .wav files are separated according to the date of the labelling in "yyyymmdd" format directories. These directories will always contain:
- labelled .wav files
- associated ".ta", ".da2" and ".ima" files, produced during the detection process, respectively in "txt", "dat", "ima" directories (see above)
- ".eti » files within a "eti" subdirectory containing the label data entered by the user

This directory path can be changed through “Modify base directory” button. This change can be imposed by the software when the user change of frequency mode in order not to mix different processing within a same RSDB.

### Base reprocessing
If the defined RSDB corresponds to an anterior version of the software, Tadarida will automatically propose an entire base reprocessing to upgrade and homogenize the database. It can however be delayed to a future execution because it can be time-consuming, except when some .wav files have been already labelled during the same day (in this case, the reprocessing of the day subdirectory is compulsory). The software indeed do not support version heterogeneity within a base subdirectory.

### Choose a .wav file
This button allows to select the .wav file to be labelled. It must have already been processed with the same version of Tadarida (see above). If not, Tadarida will ask for reprocessing and refuse labelling. Tadarida also controls coherence of associated ".da2", ".jpg", ".ta" files (see above).
The software then opens a window dedicated to fast and user-friendly labelling (see below).

### Previous
This button opens the previous .wav files in the same directory than last .wav files labelled (particularly useful when successive recordings contain the same species/events to be labelled)

### Next
This button opens the next .wav files in the same directory than last .wav files labelled (particularly useful when successive recordings contain the same species/events to be labelled)

### Update file labelling
This button allows to reopen any .wav files within the RSDB and modify its labels. Note that version compatibility is controlled before opening, and reprocessing will be asked if incompatible.

### Search
This button opens an other window allowing a research on every label fields (see below). Research criteria can be on two different fields (with an “AND” link) and each can contain two possible values (with an “OR” link).
A filter can be set on subdirectories (date), indicating a start date and/or a last date. These two dates can be equal and then the research will be done on this single date.
This search also contains a “replace” function that can be use to massively replace the text searched by another (e.g. correcting errors on species name, place, author, etc).
The output table can also be used to open the labelling window for any found reference .wav files.

## Labelling window

This window contains two parts :
### Spectrograms display
At the top, an image representing the spectrogram of the .wav files and show the DSEs
Color gradients show difference in amplitude (increasing from dark to clear), in pink within DSEs, and in blue outside DSEs (background noise).
Checkboxes allow to activate/deactivate supplementary displays:
- Grids giving both frequency and time scales
- Master points (red dots corresponding to DSEs amplitude peak in both time and frequency)
- Lines (lines describing either edges or local amplitude maxima of the DSE, see appendix for details)

Zoom buttons allow to zoom in and out on the time scale.
A double-click opens a “loop” window in which users can zoom in and out on both scales.
Time, frequency are displayed below the window according to the cursor position, whereas DSE identifier and labels appear when cursor is located close to a DSE master point.
Below the spectrogram, supplementary information is displayed:
- file name
- RSDB subdirectory (corresponding to the date of the day)
- total number of DSEs within the file, and the
- Identifiers of selected DSEs (Note that at the opening, n°1 is selected by default)
- a drop-down box indicating the species labels (see below) already entered by the user for this file. It usefully allows to select all the DSEs corresponding to one species and massively correct potential errors.

### Selecting DSEs
This spectrogram above all allows the user to select the DSEs to be labelled. Selecting single calls can be done with simple clicks close to master points, but the main interest of TadaridaL is the multiple selection through the drawing of a click and hold box. Same operations with Ctrl pressed will add supplementary DSEs to the selection or remove the same DSEs from the selection, so that complex selections of DSEs can be done directly on the spectrogram in a minimum time.
Note that when selected a DSE master point change to black.

### Labels
Below, user can enter the data corresponding to selected DSEs. Label data structure are organized in 11 fields, 7 of which are linked to the whole .wav file:
- Zone and Site are two levels of location information. Authors have commonly used « zone » field to indicate the country or region of the recording, whereas “site” usually indicates the nearest town or village.
- Material indicating the recording material used
- Confidential checkbox indicates if the recording and its label may not be published (not used at this date)
- Date of the recording
- Author of the recording
- Labeller indicate the author of the identification provided in the labels
Note that only the last saved value is stored for each .wav files, so that, if a mistake has been made in the first data entered for these fields, there is no need to reselect all the labelled DSE to correct them.
4 other label fields refer to DSE and may vary within the same .wav files:
- Species indicates the species identified as being the most probable (see confidence below) author of the vocalization selected (DSE). Note that authors have used a “noise” class for this field to label DSEs that were not from animal vocalizations. They also used six characters code in that manner: first three letters of genus then first three letters of species.
- Type indicates the type of vocalization (see type classes below)
- Confidence indicates the level of confidence that the labeler gives to the species identification (see confidence classes below)
- Comment can contain any supplementary information not provided by other label fields.
Note that most of the label fields have a drop-down box to select an existing value, and benefit from auto complete functionality according to existing list of value. Each time, a new value is provided for these fields, a confirmation is asked by the software and if confirmed, the new value is added to existing ones (except for Type field, see below).
To be as fast as possible in the labelling, all label fields keep the last entered value. A color code helps the user to see the data status:
- Blue indicates that the value shown corresponds to the last other selected DSE (and consequently currently selected DSEs have no labels)
- Black indicates that the value has been entered by the user but is not saved yet
- Green indicates that the value has been saved for at least a part of the selected DSEs
- Red indicates that the field has heterogeneous values for the selected DSEs (i.e. other values exist within the selection)
Two buttons allow to save the entered labels respectively in memory and in the label file (.eti).
If some labels have been saved but not the .eti file, a message box will propose to do so.
A « Close » button allows the user to close the labelling window, with or without saving its label data.

#### Type classes
Authors have chosen very simple classification of vocalization type in order to facilitate replication among a community of bioacousticians who could share their respective RSDB. They intend to identify different behavior class
- “echolo” refer to echolocation calls (e.g. bats)
- “terr” refer to explicitly territorial vocalization (used only for birds)
- “social” refer to any other social vocalization
- “buzz” refer to feeding buzz of bats
- “elec” refer to electronical parasites
- “mec” refer to any other noise (mechanical)
This simple classification can however be changed by editing the « type.txt » contained within the software directory and adding new codes. We do not recommend to remove or aggregate these codes, to ensure compatibility with other RSDBs.

#### Confidence classes
Authors have also chosen a simple classification of confidence to facilitate replication among a community of bioacousticians who could share their respective RSDBs.
1 indicates a high risk of misidentification in the species label (> 10%)
2 indicates a medium risk of misidentification in the species label (1-10%)
3 indicates a low risk of misidentification in the species label (< 1%)
4 indicates a particularly low risk of misidentification considering the species, thanks to complementary information, yet the identification is still uncertain (e.g. recordings done close to a known roost)
5 indicates recordings of individuals identified with certainty and by other means than the recording itself (usually visually)

### Output

After saving, all entered label information is then stored in ".eti” files within a "eti" subdirectory.
Call identifiers stored in both .eti and .ta files ensure data coherence between labels and extracted features and allow to build an automatic classification process (see Tadarida-C).

### Reprocessing of the whole RSDB
Reprocessing your RSDB is necessary every time a Tadarida-L upgrade modify either the detection or the feature extraction process.
If the detection process is modified, delimitation of DSEs can change. Coherence between original and “modified” labels is ensured through comparison of master points in time and frequency.
To loose the least possible information through successive rematching, label rematching is always based on the original label files (i.e. earliest Tadarida version)
Thus, original structural data (.da2) and label (.eti) files are stored within RSDB in subdirectories indicating the TadaridaL version originally used
At the end of the reprocessing, the number of rematched DSEs labels is displayed in a message box.
Details of this reprocessing are stored in retreat.log and tadarida.log files.

## Tadarida-L architecture

Tadarida-L is an extended version of Tadarida-D to handle sound events labelling and reference sound database (RSDB) constitution (in addition to sound events detection and features extraction as done by Tadarida-D).
This application is structured around 4 classes (corresponding to each .cpp file):

### TadaridaMainWindow

This class generates the main window of the software and displays main user settings.
The left half of the window contains all the input settings of the detection process: the directory path of the .wav files to be processed, and optional settings (see Tadarida-L manual). It calls threads of the Detec class for .wav files treatment.
The right half of the window displays the labelling interface. It calls the following Fenim class.

### Detec and Detectreatment

Both Detec and Detectreatement classes have the same purpose in Tadarida-L as they have in Tadarida-D. Detectreatment class is strictly identical. Detec class here has just one additional function: it handles the generation of supplementary output files (in extended mode, see Tadarida-L manual): spectrogram images (.jpg) and DSEs data (.da2). These files are used by Fenim class as input information (see Fig. 2).

The object of Detec class retrieves provided settings and creates the object of DetecTreatment class that will handle the output processing (generation of features tables).
The run() method (executed by pdetec [i] -> start () ;) organizes treatment.
It calls for each .wav file to be processed, the treatOneFile method, which launches CallTreatmentsForOneFile(...) method of DetecTreatment class.
Note that the division of tasks between the Detec and Detectreatment classes avoid a duplication of code in the DetectTreatment class between Tadarida-D and Tadarida-L projects

After initialization, the CallTreatmentsForOneFile method handles the processing of each .wav file by successively calling the following methods:

#### openWavFile and computeFFT
These first two methods basically read .wav files and compute from it a time-frequency matrix using Fast Fourier Transformation (FFTW3 library).
FFT window size is set according to sample rate in order to get the most possibly constant frequency and time resolutions: respectively 0.2-0.4 ms and 0.6-1.2 kHz in HF mode, and 2-4 ms and 60-120 in LF mode.
FFT overlap is by default set to 75 % as an optimal trade-off between the amount of information collected and the computing speed.

#### correctNoise

This pre-processing step consists in two successive treatments: ignoring silence and frequency equalizing.
Ignoring silence consists in detecting periods in .wav files when no acoustic signals are recorded. This commonly happens when recording the output of some ultrasound detectors involving a trigger (e.g. Pettersson D240X©), but can also happens with any recorder when for example the microphone is accidentally unplugged. Note that periods when microphone output is recorded without any source of sound are not considered silence and thus are not ignored since they can provide good information on background noise level (see below).
Frequency equalizing is performed by substracting to each frequency line in the matrix its proper noise floor (5%-quantile in amplitude). This simple operation has strong consequences for sound event detection and several advantages:
It usefully reduces biases generated by heterogeneity in recorders output, especially gain and variable microphone sensitivity across frequencies, and thus makes Tadarida-D functional over a wide range of recorders.
It erases narrowband electronical noise without any loss of hearable sound events.
It separates sound events even when a chorus of individuals produce constantly a large amount of amplitude on a frequency band (a common situation with insects)

#### shapesDetects

This method determines the detection of sound events. A detected sound event (DSE) is here defined as a set of elements of the frequency-time matrix and aims at isolating an acoustic signal in both frequency and time coming from a single acoustic source. The process follows an hysteresis function involving two amplitude thresholds:
the high threshold first determines the presence of a DSE, i.e. every element of the matrix over this threshold are part of a DSE.
the low threshold second determines the limit of DSEs. An element in the matrix is indeed part of a DSE if it meets the following conditions: being over this low threshold AND (being adjacent in rows (frequency band) to an element of the DSE OR being less than 5 columns (approx. 1.5 ms in HF mode and 15 ms in LF mode) away from an element of the DSE).

Authors found optimal values at 26 dB for the high threshold and 20 dB for the low threshold. These values produced very low rates of false positives (detection in the background noise) and false negatives (hearable sound event not detected).

Highest amplitude value among the elements within the DSE defines the master point. At this stage, sound events are filtered according to the frequency mode chosen: 8 to 250 kHz for high frequency and 0.8 to 25 kHz for low frequency. Note that the high frequency range chosen covers every known vocalization of bats and bush-crickets and the low frequency range covers most other animal vocalization.

#### detectsParameter2 and saveParameters

These two method consist in the computing and saving of 269 numerical features on each DSEs. These features are stored in tables within specific .ta files (tab separated text format, Fig. 2). See appendix for the definition of each numerical features. Note that some of these numerical features are based on proven methods in bioacoustics whereas the others are based on an empirical approach. Authors have indeed looked for the most discriminant features for the most problematic pairs of species (i.e. those with highest error rates, see below) and added some new custom features each time they were needed to improve classification.

### Fenim

Fenim class handles:
- spectrogram display that can be zoomed in and out on two separate Windows
- graphical multiple selection of DSEs
- label data entry (11 fields: species, confidence, location, etc. see Tadarida-L manual)
- saving data in standard tables (.eti) linked to extracted features.

This labelling process allows the user to quickly generate a standardized RSDB that can be shared with other users, and used to build their own classifier (Fig. 2).

Note that Tadarida-L has been built in an evolutive way so that both detection and feature extraction process can be drastically changed with no loss of information in users RSDBs.

If the defined RSDB corresponds to an anterior version of the software, Tadarida will indeed propose an entire base reprocessing to upgrade and homogenize the database.
News DSEs will be matched according to their previous and new structural data (.da2)
Note that, original label data (.eti files) and original structural data (.da2) are always stored in RSDB, in subdirectories indicating the version originally used, so that if a previously labelled DSE found no match in a current version of the detection process, it could be nevertheless retrieved in another future upgrade.

## Appendix : features list

Name	Definition	Version / (1)
StTime	Start time of the detected sound event (DSE)	X
Dur	DSE duration	X
PrevSt	Time difference between starts of the DSE and the previous one	X
FMin	Minimum frequency	X
FMax	Maximum frequency	V1
BW	FMax-FMin	X
FreqMP	Frequency of the master point (i.e. single element with the highest amplitude)	V1
PosMP	Time Position of the master point (in fraction of the DSE duration)	X
FreqPkS	Frequency of maximum energy (frequency energy is here calculated as the sum of amplitude among single frequency bands)	V1
FreqPkM	Frequency of maximum energy (frequency energy is here calculated as the mean of amplitude among single frequency bands)	V1
PosPkS	Time position of the element with maximum amplitude at FreqPkS (fraction of the DSE duration)	V1
PosPkM	Time position of the element with maximum amplitude at FreqPkM (fraction of the DSE duration)	V1
FreqPkS2	Frequency of the element with maximum amplitude at PosPkS time.	V1
FreqPkM2	Frequency of the element with maximum amplitude at PosPkM time.	V1
PrevMP1	Time difference between master points of the DSE and the previous one	X
PrevMP2	Time difference between master points of the DSE and the previous one whose master point is between FMax and FMin, and conversely its FMin-FMax interval contains FreqMP of the current DSE	X
NextMP1	Time difference between master points of the DSE and the next one	X
NextMP2	Time difference between master points of the DSE and the next one whose master point is between FMax and FMin, and conversely its FMin-FMax interval contains FreqMP of the current DSE	X
Amp1	Average amplitude among time windows within the 1st quarter of the DSE	X
Amp2	Average amplitude among time windows within the 2nd quarter of the DSE	X
Amp3	Average amplitude among time windows within the 3rd quarter of the DSE	X
Amp4	Average amplitude among time windows within the last quarter of the DSE	X
NoisePrev	Average amplitude among the elements neighbouring the DSE on the left on a 3-element width (approx. 1 ms before)	X
NoiseNext	Average amplitude among the elements neighbouring the DSE on the right on a 3-element width (approx. 1 ms after)	X
NoiseDown	Average amplitude among the elements neighbouring the DSE on the top on a 3-element width (approx. 2 kHz above)	X
NoiseUp	Average energy among the elements neighbouring the DSE on the bottom on a 3-element width (approx. 2 kHz below)	X
CVAmp	Coefficient of variation of Amp1, Amp2, Amp3 and Amp4	X
Dbl8	Amplitude difference between the DSE and low-frequency noise (=everything below 8kHz)	X
Stab	An index of amplitude stability around the master point: average amplitude change between neighbouring elements within the DSE, inversely weighted by distance from Master Point	X
HeiET	Number of time windows within the DSE, whose cumulated amplitude exceeds 80% of the cumulated amplitude of the master point time window	X
HeiEM	Number of time windows within the DSE, whose mean amplitude exceeds 80% of the mean amplitude of the master point time window	X
HeiRT	HeiET divided by total number of time windows	X
HeiRM	HeiEM divided by total number of time windows	X
HeiETT	Number of time windows, after master point and within the DSE, whose cumulated amplitude exceeds 80% of the cumulated amplitude of the master point time window	V1
HeiEMT	Number of time windows, after master point and within the DSE, whose mean amplitude exceeds 80% of the mean amplitude of the master point time window	X
HeiRTT	HeiETT divided by total number of time windows	X
HeiRMT	HeiEMT divided by total number of time windows	X
MedInt	Median of intervals between DSEs of similar frequency bands (i.e. whose master point is within +/- 2 frequency bands around the current DSE master point, corresponding to an approx. 3 kHz interval)	V1
Int25	1st quartile of intervals between DSEs of similar frequency bands (i.e. whose master point is within +/- 2 frequency bands around the current DSE master point, corresponding to an approx. 3 kHz interval)	X
Int75	3rd quartile of intervals between DSEs of similar frequency bands (i.e. whose master point is within +/- 2 frequency bands around the current DSE master point, corresponding to an approx. 3 kHz interval)	X
RInt1	Int75 / Int25	X
IntDev	Median deviation from MedInt among the “similar frequency” (see MedInt above) intervals	V1
SmIntDev	Median deviation from Int25 among the half smallest “similar frequency” (see Int25 above) intervals	X
LgIntDev	Median deviation from Int75 among the half largest “similar frequency” (see Int75 above) intervals	X
VarInt	IntDev/MedInt	X
VarSmInt	SmIntDev/Int25	X
VarLgInt	LgIntDev/Int75	X
RIntDev1	LgIntDev/SmIntDev	X
EnStabSm	Average change of amplitude between adjacent elements on a square of 7 x 7 elements around the master point (~2 ms - ~5kHz)	X
EnStabLg	Average change of amplitude between adjacent elements on a square of 21 x 21 elements around the master point (~6 ms - ~11kHz)	X
HetX	Proportion of change of amplitude slope, among each set of 3 consecutive elements along the time axis.	X
HetY	Proportion of change of amplitude slope, among each set of 3 consecutive elements along the frequency axis.	V1
HetXr	Idem HetX but restricted to the 7 frequency bands around the master point.	V1
HetYr	Idem HetY but restricted to the 7 time windows around the master point.	X
HetYr2	Average amplitude difference between adjacent elements	V1
HetCMC	Proportion of consecutive time windows where average amplitude slope changes	X
HetCMD	Average difference of average amplitude between each pair of consecutive time windows	X
HetCTC	Proportion of consecutive time windows where cumulated amplitude slope changes	X
HetCTD	Average difference of cumulated amplitude between each pair of consecutive time windows	X
HetCMnP	Number of local average amplitude maxima among time windows	V1
HetCMfP	Density of local average amplitude maxima among time windows	X
HetCTnP	Number of local cumulated amplitude maxima among time windows	V1
HetCTfP	Density of local cumulated amplitude maxima among time windows	X
HetPicsMAD	Median interval between local average amplitude maxima among time windows	V1
HetPicsMALD	1st quartile of intervals between local average amplitude maxima among time windows	X
HetPicsMABD	3rd quartile of intervals between local average amplitude maxima among time windows	X
HetPicsMRBLD	HetPicsMABD / HetPicsMALD	X
HetPicsTAD	Median interval between local cumulated amplitude maxima among time windows	V1
HetPicsTALD	1st quartile of intervals between local cumulated amplitude maxima among time windows	V1
HetPicsTABD	3rd quartile of intervals between local cumulated amplitude maxima among time windows	X
HetPicsTRLBD	HetPicsTABD / HetPicsTALD	X
VDPicsM	Median deviance from HetPicsMAD among intervals between local average amplitude maxima among time windows	V1
VLDPicsM	1st quartile deviance from HetPicsMAD among intervals between local average amplitude maxima among time windows	V1
VBDPicsM	3rd quartile deviance from HetPicsMAD among intervals between local average amplitude maxima among time windows	V1
VDPPicsM	VDPicsM / HetPicsMAD	V1
VLDPPicsM	VLDPicsM / HetPicsMALD	X
VBDPPicsM	VBDPicsM / HetPicsMABD	X
VDPicsT	Median deviance from HetPicsMAD among intervals between local cumulated amplitude maxima among time windows	V1
VLDPicsT	1st quartile deviance from HetPicsMAD among intervals between local cumulated amplitude maxima among time windows	V1
VBDPicsT	3rd quartile deviance from HetPicsMAD among intervals between local cumulated amplitude maxima among time windows	V1
VDPPicsT	VDPicsT / HetPicsTAD	V1
VLDPPicsT	VLDPicsT / HetPicsMALD	X
VBDPPicsT	VBDPicsM / HetPicsMABD	X
Ramp_2_1	Ratio of average amplitude between the elements whose frequency is twice that of the DSE and those of the current DSE	X
Ramp_3_1	The same for triple frequency	X
Ramp_3_2	The same for frequency multiplied by 1.5	X
Ramp_1_2	The same for half frequency	X
Ramp_2_3	The same for frequency multiplied by 2/3	X
Ramp_4_3	The same for frequency multiplied by 4/3	V1
RAN_2_1	Ratio of cumulated energy between the elements surrounding (3 elements width) those whose / frequency is twice that of the DSE and the elements whose / frequency is twice that of the DSE	X
RAN_3_1	The same for frequency multiplied by 3	X
RAN_3_2	The same for frequency multiplied by 1.5	X
RAN_1_2	The same for half frequency	X
RAN_2_3	The same for frequency multiplied by 2/3	X
RAN_4_3	The same for frequency multiplied by 4/3	X
RAHP2	Ratio of average bandwidth between the first half before the master point of the DSE and the following. The first nine time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted before the master pointe	V1
RAHP4	Ratio of average bandwidth between the first quarter before the master point of the DSE and the following. The first six time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	V1
RAHP8	Ratio of average bandwidth between the first 1/8 before the master point of the DSE and the following. The first four time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	V1
RAHP16	Ratio of average bandwidth between the first 1/16 before the master point of the DSE and the following. The first three time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	V1
RAHE2	Ratio of average amplitude between the first half of the DSE and the following. The first nine time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	V1
RAHE4	Ratio of average amplitude between the first quarter of the DSE and the following. The first six time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	X
RAHE8	Ratio of average amplitude between the first 1/8 of the DSE and the following. The first four time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	V1
RAHE16	Ratio of average amplitude between the first half of the DSE and the following. The first three time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	V1

‘X’ = versions n°1 and 2 - ‘V1’ = only version n°1
Following features are based on the link between two DSEs who could potentially be harmonics of the same DSE. The conditions for two DSEs to be potential harmonics are that both master points are included in the time duration of both DSE. For each DSE, both an upper harmonic (Hup_) and a lower harmonic (Hlo_) are searched for. If no match is found, corresponding features equal to 0. If several matches are found, the closest DSE in FreqMP is selected.
Hup_RFMP	Ratio of FreqMP between “potential harmonic” (see definition above) and the DSE	X
Hup_PosMP	Time position of the Master Point of the potential upper harmonic (fraction of the DSE duration)	V1
Hup_PosSt	Time position of the start of the potential upper harmonic (fraction of the DSE duration)	V1
Hup_PosEn	Time position of the end of the potential upper harmonic (fraction of the DSE duration)	V1
Hup_AmpDif	Amplitude difference between the DSE and its potential upper harmonic	X
Hup_RSlope	Ratio of MC_Slope (see below) between potential upper harmonic and the DSE	V1
Hlo_RFMP	Same parameters for potential lower harmonic	V1
Hlo_PosMP		V1
Hlo_PosSt		V1
Hlo_PosEn		X
Hlo_Ampdif		X
Hlo_RSlope		V1

Line-based features
At last, 5 linear descriptors of each DSE are drawn. They correspond of a subset of elements of the DSE basically drawing a line on the spectrogram

1)  	MC is the line of elements which have the maximum amplitude on each time window (note that these elements may not be adjacent on the spectrogram matrix).
2)  	StE is the starting edge of the DSE (elements forming the left edge of the DSE)
3)  	UpE is the upper frequency edge of the DSE
4)  	DoE is the lower frequency edge of the DSE
5)  	StC is formed by the first elements forming a local amplitude maximum on each frequency band (matrix line). In many cases, StC significantly better describes modulated signals than other line types, even in case of intense and numerous echoes.
Note that ending edge is not taken into account since it is mainly driven by the echoes and supposed to give little valuable information because of this.

Tableau 2

Suffix	Definition	CM	CS	CN	CO	CO2
_Dur	Duration				V1	V1
_FMax	Maximum frequency	V1	V1
_FMin	Minimum frequency	V1		V1
_BW	Bandwidth (FMax-FMin)	V1	V1	V1
_FPk	Frequency of maximum amplitude					V1
_FPkD	Difference of _FPk with previous DSE					X
_TPk	Time of amplitude peak (in fraction of line duration)					X
_Slope	Modulation Slope	X	X	X	X	X
_ISlope	1/Slope				V1	X
_HCF	Frequency of the point of maximum change of slope over/before FlF (see below). Calculated with a least square error from a two segments regression.	V1	V1	V1	V1	V1
_THCF	Time of the point which gaves “HCF” (in fraction of line duration)	X	X	X	X	X
_FlF	Frequency of the flattest part of the line (calculated on 5 consecutive time windows). If several frequencies get a 0 slope, FlF takes the value of longest null slope.	X	X	X	V1	V1
_LCF	Frequency of the point of maximum change of slope under/after FlF. Calculated with a least square error from a two segments regression.	V1	V1	V1	V1	V1
_UpSl	Slope of the upper part of the line (over HCF)	X	X	X	X	X
_LoSl	Slope of the lower part of the line (below HCF)	X	X	X	X	X
_StF	Start frequency (first element in time)	V1
_EnF	End frequency (last element in time)	V1
_StSl	Start Slope	X	X	X	X	X
_EnSl	End Slope	X	X	X	X	X
_FlSl	Slope at the FlF point	X				X
_FPSl	Slope at the point of maximum amplitude	V1	X	X	X	V1
_CeF	Half-time Frequency	V1	V1	V1
_5dBBF	Frequency of the farthest point before FPk and less than 5 dB below peak amplitude	V1				V1
_5dBAF	Frequency of the farthest point after FPk and less than 5 dB below peak amplitude	V1				V1
_5dBBW	Difference between 5dBBF and 5dBAF	X				X
_5dBDur	Time difference between 5dBBF point and 5dBAF point	X				X
SDC	Cumulated changes in frequency slope. Calculated as the sum of abs((f(x+1)-f(x) - (f(x)-f(x-1))) where (f(x) is the frequency of the element x of the line.	V1	V1	V1	V1	V1
SDCR	SDC / Dur	X	X	X	X	X
SDCRY	SDCR / BW	V1	V1
SDCRXY	SDCRY / Dur	X	X
SDCL	Cumulated changes in frequency slope of the part of the line before the first eventual ascent succeeding the master point	X	V1
SDCLR	SDCL / Dur	V1	V1
SDCLRY	SDCLR divided by frequency amplitude	V1	V1
SDCLRXY	SDCLRY / Dur	V1	V1
SDCLOP	Cumulated changes in frequency slope of the “main slope” of the line. The “main slope” is defined as the part of the line which contains the master point and has no change of slope direction.	X	X
SDCLROP	SDCLOP / Dur	X	X
SDCLRYOP	SDCLOP divided by frequency amplitude of the pan	V1	X
SDCLRXYOP	SDCLRYOP divided (a second time) by duration	V1	V1
SDCLWB	Cumulated changes in frequency slope of the part of the line between the middle between start and master point and the first eventual ascent after master point	V1	X
SDCLRWB	SDCLWB / Dur	X	V1
SDCLRYWB	SDCLRWB divided by frequency amplitude	V1	V1
SDCLRXYWB	SDCLRWB divided (a second time) by duration	V1	V1
SDCLOPWB	Cumulated changes in frequency slope of the part of the line between the middle of this pan before master point and the end of it	V1	V1
SDCLROPWB	SDCLOPWB / Dur	V1	V1
SDCLRYOPWB	SDCLROPWB divided by frequency amplitude	V1	V1
SDCLRXYOPWB	SDCLWB divided (a second time) by duration	X	V1
SDCL_DNP	SDCL divided by the number of changes of direction of the line (positive/negative)	V1	V1
SDCLR_DNP	SDCL_DNP / Dur	X	X
SDCLRY_DNP	SDCLR_DNP divided by frequency amplitude	V1	X
SDCLRXY_DNP	SDCLRY_DNP divided (a second time) by duration	V1	V1
ELBPOS	Duration of line to the moment where the line makes a “bend” divided by the duration of the line before the first eventual ascent of the line. A “bend” is defined as the first element x where the slope ratio between 3 elements before and 3 elements after x is under 0.6	X	X
ELBSB	Slope of the part of the line ending at the first bend determined by local slopes (ELBPOS)	X	X
ELB2POS	The same as ELBPOS, but the bend id determined by the global slopes before and after the bend	X	X
ELB2SB	Slope of the part of the line ending at the first bend identified by global slopes (ELB2POS)	X	X
RAF	Ratio of time windows average frequency before the master point and after	V1
RAE	Ratio of time windows average amplitude before master point and after	V1
RAFE	RAF + RAE	X
RAFP	Ratio of the sums of time window average amplitude before and after master point	V1
RAFP2	Ratio of the sums of amplitude before and after master point	V1
RAFP3	Ratio of the sums of time windows average amplitude weighted by amplitude (of the point of the line), before and after master point	X
SBMP	Slope between the beginning of the line and the master point	X
SAMP	Slope between the master point and the end of the line	X
SBAR	SBMP/SAMP	X